## Slide 1
Effect of Entrapped Non-condensable Gas on Shock-Driven Droplet Deformation:
Implications for Hypersonic Rain Environments
Juan P. Roldan1, 2, Brendon A. Cavainolo1, Rebecca C. Shannon3, Guillermo A. Jaramillo2, Sheryl M. Grace3, Michael P. Kinzel1
1Embry-Riddle Aeronautical University, Daytona Beach FL, 32114, USA
2Universidad del Valle, Cali, Valle del Cauca, Colombia
3Boston University, Boston, MA, 02215, USA

## Slide 2: Motivation – Rain Erosion
Hypersonic glide vehicles encounter atmospheric hydrometeors during terminal descent at 0–7 km
  Micron cloud droplets to millimeter raindrops
Cumulative droplet impacts roughen the surface → early boundary-layer transition → heating/drag/control-authority penalties
These margins are already thin in air-breathing systems
Figure: Schematic of atmospheric droplets interacting with the bow shock of a hypersonic vehicle before and after shock passage. Adapted from Aguilera 2023.
Dworzanczyk 2025

## Slide 3: Motivation – Rain Erosion
Impact loading scales with
A single 2mm raindrop can exert up to 40kN of force
Figure: View of hypersonic vehicle terminal dive phase (Aguilera 2023).
Figure: 4mm droplet impact on radome at Mach 3 (Moylan 2013).
Figure: Vehicle nosetip post flight through clouds (Sandia National Labs).

## Slide 4: Motivation – Drop Acoustics and Rain Formation
Shock transmission  internal wave dynamics
  Reflections / expansion waves
Cloud droplets and raindrops form through condensation on suspended aerosol particles
  May trap microscopic gas pockets (heterogenous nuclei)
Particle | Diameter, μm | Terminal velocity, m s-1
Typical condensation nucleus | 0.2 | 1.0 10-6
Typical cloud drop | 20 | 0.01
Cloud drop / raindrop conventional borderline | 100 | 0.27
Typical raindrop | 2000 | 6.50
Particle | Diameter, μm | Terminal velocity, m s-1
Typical condensation nucleus | 0.2 | 
Typical cloud drop | 20 | 0.01
Cloud drop / raindrop conventional borderline | 100 | 0.27
Typical raindrop | 2000 | 6.50
Table: Typical sizes and terminal velocities of liquid particles in clouds (Aguilera 2023).
Figure: Progression of droplet internal waves (Biasiori-Poulanges 2023).

## Slide 5: Scope and Objectives
Can the consideration of pre-existing nuclei measurably affect droplet deformation?
Computationally study the role of pre-existing non-condensable gas nuclei in the early-time response of a shock-loaded liquid droplet.
Objectives:
Benchmark the compressible multiphase framework
Characterize the “clean” shock-droplet baseline
Quantify the mechanical response of embedded gas nuclei
Assess the impact of the bubble response on the droplet pressure field and deformation

## Slide 6: Literature: Cavitation and Entrained Nuclei
Internal pressure focusing can activate cavitation or gas nuclei, but existing studies have not isolated the mechanical response of pre-existing non-condensable nuclei.
Sembian et al., 2016
Provided direct shock-water-column evidence of internal wave focusing and cavitation
Forehand et al., 2023-2024
Compared simulations with and without cavitation modeling
One-way coupling bubble dynamics
Briggs / Aguilera, 2023-2026
Experiments of degassed, ambient, and doped droplets (~Mach 3, D=1-3mm)
Limited diagnostic, little evidence

## Slide 7: Literature: Knowledge Gaps
Prior work identified cavitation-prone regions and droplet breakup mechanisms but did not resolve the direct feedback of pre-existing gas nuclei.
Isolated nuclei response
Two-way coupled multi-nuclei effects
Early pressure field feedback
Gap 1:
Gap 2:
Gap 3:

## Slide 8: Methodology: Computational Setup
All simulations are performed in cylindrical coordinates under an axisymmetric assumption.
Boundary conditions:
The bottom boundary is an axis of symmetry
All other boundaries are non-reflecting boundaries
Initial conditions:
Shocked air set by Rankine-Hugoniot jump conditions into quiescent, ambient air
Figure: Computational domain, normalized by droplet diameter, D.

## Slide 9: Methodology: Simulation Matrix
Parameter space: For a 1mm droplet, , ,
A clean case is run at each Mach, 36 doped cases
Parameter | Values |  |  | 
Shock Mach, | 3 | 5 | 7 | -
Initial bubble radius, | 0.1 | 0.2 | 1 | 2
Number of bubbles, | 10 | 100 | 1000 | -
Parameter | Values |  |  | 
 | 3 | 5 | 7 | -
 | 0.1 | 0.2 | 1 | 2
 | 10 | 100 | 1000 | -
Table: Shock-droplet simulation matrix. This spans the doped cases.
Figure: Sub-grid Lagrangian bubble representation.
: Sub-grid Lagrangian bubble
D = 1 mm

## Slide 10: Methodology: Number Density and Void Fraction
Number density:
For yields , respectively
Void Fraction:
10 |  |  |  | 
100 |  |  |  | 
1000 |  |  |  | 
10 |  |  |  | 
100 |  |  |  | 
1000 |  |  |  | 
Table: Initial global gas void fraction for the bubble-loading parameter sweep.

## Slide 11: Methodology: The Numerical Model
The present simulations are performed in the Multi-Component Flow Code (MFC)
Open-source, high-order, compressible multiphase solver
Sub-grid bubble models
Highly parallel
Resolved Eulerian phase interface:
Reduced five-equation diffuse-interface formulation of Allaire et al. 2002.
Figure: Sharp and diffuse interface of a multiphase flow (Adebayo 2025).

## Slide 12: Methodology: Interface Formulation
Allaire’s Model ()
Mechanical equilibrium with an isobaric closure
Passively advected volume fraction
  High numerical robustness
Strictly conservative volume-fraction
Strict entropy consistency is not guaranteed
Kapila’s Formulation ()
Thermodynamically consistent treatment in transition zones
  However, the smeared region is not physically a transition zone
  Unclear whether this “fix” is physical
Needs additional conservative treatment
Wood’s speed of sound is non-monotonic

## Slide 13: Methodology: The Numerical Model
Each material is closed with a stiffened-gas equation of state
The material properties are listed below:
Viscous stresses and surface tension are neglected in the resolved Eulerian equations.
Quantity | Air / bubble gas | Liquid water
Density, | 1.17 kg m-3 | 1000 kg m-3
Ratio of specific heats, | 1.4 | 4.4
Stiffened pressure, | 0 | 600 MPa
Quantity | Air / bubble gas | Liquid water
 | 1.17 kg m-3 | 1000 kg m-3
 | 1.4 | 4.4
 | 0 | 600 MPa
Table: Equation-of-state and material parameters used in the shock-droplet simulations.

## Slide 14: Methodology: Euler-Lagrange Bubble Model
The doped-droplet cases contain Lagrangian gas nuclei embedded inside the initially liquid droplet.
Each nucleus is modeled as a spherical sub-grid bubble
The bubbles do not advect
The resolved Eulerian field provides the local driving pressure
Bubble volume change feeds back to the Eulerian field through source terms
Figure: Sub-grid spherical bubble model and two-way Eulerian–Lagrangian coupling used to evolve the embedded gas nuclei.

## Slide 15: Methodology: Keller-Miksis-Type Model
The sub-grid bubble dynamics:
Bubble radius, , is evolved with a Keller-Miksis-type equation
Extends the Rayleigh–Plesset equation (RPE) by retaining first-order liquid compressibility effects
  As , the equation reduced to RPE
Appropriate for spherical sub-grid nuclei in a weakly compressible liquid
Liquid inertia + compressibility/viscous correction
Nonlinear radial inertia
Net pressure driving, corrected for finite sound speed
Time-varying pressure/ acoustic radiation correction

## Slide 16: Methodology: Numerical Methods
The Eulerian equations are discretized on a structured grid using a finite-volume formulation.
A constant CFL value of 0.1 is used in all simulations.
Numerical Component | Method Used
Face reconstruction | 2nd order MUSCL + van Leer limiter
Interface treatment | THINC interface sharpening
Riemann Solver | HLLC
Time-integration | SSP-RK3 (TVD)
Flow-bubble coupling | Operator splitting
Table: Summary of numerical methods used for the Eulerian flow solver and sub-grid bubble dynamics.
Figure: Numerical results for a planar Mach onto a gas bubble. With THINC (left) and without THINC (right) are both shown (Shyue-Xiao 2014).

## Slide 17: Methodology: Strang Splitting
The Scheme:
For , each time step performs three sub-steps:
Source half-step ()
Flux full-step ()
Source half-step ()
Motivation:
Two physics with very different timescales:
  Fluid: pressure waves, advection, governed by CFL timestep
  Bubbles: Oscillate much faster (stiff)
Integrating both together forces a tiny everywhere  expensive
Solution: Treat as separate operators
Key Points:
Half + full + half achieves 2nd-order splitting accuracy
Full + full achieves 1st-order
Steps 1 & 3 subcycle internally with an adaptive embedded RK scheme
  Takes as many steps as needed to reach exactly
Step 2 uses the standard TVD-RK fluid update at the CFL

## Slide 18: Methodology: Code Extensions
Azimuthal mapping operator to each 3D bubble:
Preserves equivalent axisymmetric bubble volume
Deposits bubble source terms consistently in cylindrical coordinates
Resulting axisymmetric void fraction field:
Figure: Axisymmetric mapping of a 3D Lagrangian bubble kernel onto neighboring FVM cells (Maeda-Colonius 2018).
Cylindrical Euler-Lagrange Bubble Model: allows Lagrangian gas nuclei to be used in the axisymmetric formulation used for the simulations

## Slide 19: Methodology: Benchmarking
Benchmarking Against Shock-Water Column Experiments:
Sembian 2016 studies the interaction of a planar shock (Mach = 1.75 and 2.4) onto a droplet column of diameter
Large droplet allows for the observation of key internal acoustics
Numerical schlieren is compared directly to the experimental shadowgraph
  Comparison of transmitted shocks, reflected waves, expansion regions, slip surfaces, and triple-point/Mach-stem structures
Excellent agreement is observed
Figure: 22mm water column of Sembian 2016.

## Slide 20: Methodology: Benchmarking
Benchmarking Against Shock-Water Column Experiments:
Figure: Comparison between experimental shadowgraph images from the Mach 2.4 shock-water-column experiment of Sembian et al. and numerical schlieren fields from the MFC simulation.
Transmitted shock
REx Focusing
Secondary Reflection
Mach-Mach collision
Re-circulation zone
Reflected expansion waves (REx)

## Slide 21: Methodology: Mesh Independence
Performed on a clean droplet in our case of interest
Mach 7 is chosen for the study as it produces the largest pressure gradients within the droplet
A refinement factor of is used
Shock-arrival time, peak pressure, pressure decay, and area-averaged pressure response across mesh levels was compared
All meshes show close agreement, hence the medium mesh was chosen
Mesh | Cells / | Grid size | 
Coarse | 300 |  | 3.33
Medium | 400 |  | 2.50
Fine | 600 |  | 1.67
Mesh |  |  | 
Coarse | 300 |  | 
Medium | 400 |  | 
Fine | 600 |  | 
Table: Mesh levels used in the shock-droplet mesh-independence study.

## Slide 22: Methodology: Mesh Independence
Nearest-cell pressures

## Slide 23: Methodology: Summary of Assumptions
Geometry / interface:
Axisymmetric geometry
Diffuse-interface formulation with interface sharpening
Droplet-scale surface tension neglected
Sub-grid nuclei model:
Bubbles are modeled as spherical sub-grid nuclei
Bubbles remain fixed in space; no stochastic correction
No asymmetrical collapse
Bubble-bubble interaction only through the resolved pressure field
Thermodynamic / transport simplifications
Non-condensable gas nuclei
No vapor production, mass transfer, and phase change
Polytropic bubble gas response
Neglecting viscosity in Eulerian phase

## Slide 24: Clean Results: Non-dimensionalization
Shock-droplet interaction in the absence of dissolved gas nuclei.
All quantities are presented in the dimensionless time:
Where is the Ranger-Nichols aerobreakup timescale:
Define acoustic crossing time:
Quantity | Ms = 3 | Ms = 5 | Ms = 7
 | 1.044 | 2.929 | 5.757
 | 772.5 | 1390.6 | 1986.5
 | 19.27 | 9.40 | 6.31
 | 0.615 | 0.614 | 0.613
 | 0.0319 | 0.0653 | 0.0971
Quantity | Ms = 3 | Ms = 5 | Ms = 7
 | 1.044 | 2.929 | 5.757
 | 772.5 | 1390.6 | 1986.5
 | 19.27 | 9.40 | 6.31
 | 0.615 | 0.614 | 0.613
 | 0.0319 | 0.0653 | 0.0971
Table: Key acoustic timescales.

## Slide 25: Clean Results: Internal Wave Structure
Figure: Space-time diagram of axial centerline pressure for the three clean-baseline cases. Left: Mach 3; center: Mach 5; right: Mach 7.

## Slide 26: Clean Results: Peak Pressure
Figure: Center-probe pressure history plotted against time normalized by the acoustic crossing time. Left: absolute pressure. Right: pressure normalized by case-specific post-shock pressure.

## Slide 27: Clean Results: Rarefaction
Figure: Minimum centerline pressure along the droplet axis, minimized over Left: absolute minimum pressure. Right: normalized by .
Each acoustic reflection generates a rarefaction wave that propagates back into the droplet and produces tensile pressures.

## Slide 28: Clean Results: Early Droplet Deformation
Figure: Numerical schlieren left and numerical shadowgraph right of the early-time droplet deformation.
Early-time droplet deformation:
Noticeable flattening on the windward face
Rim roll-up and lip formation
RTP mode formation
Dimple forming at the aft interface
Numerical artifact*:
Upstream-face dimple
Rim roll-up
Windward face flattening
Lip formation
RT modes
Aft-interface dimple
Upstream-face dimple*

## Slide 29: Doped Results: Spatial Selectivity of Activation
The normalized underpressure integral predicted that bubble activation should be concentrated in the downstream half of the droplet.
The simulations confirm this prediction
Consider the Mach 5, , case:
Bin the 100 bubbles by initial position
Figure: Spatial bins based on initial streamwise nucleus location, showing median and maximum bubble growth.

## Slide 30: Doped Results: Spatial Selectivity of Activation
Figure: Scatter plots of normalized bubble growth at Mach 5. Left: . Right: .
Downstream half of the droplet shows most bubble activation

## Slide 31: Doped Results: Absolute Bubble Growth
Figure: Absolute maximum bubble radius in for all doped cases.
Mach number:
Strongest influence on peak bubble growth (Mach ↑, ↑)
Initial bubble radius:
Significant effect on
~constant for a given Mach
Bubble population:
Least effect on peak bubble growth
seems to limit peak bubble growth when compared to other population sizes

## Slide 32: Doped Results: Pressure Perturbations
The volumetric growth and collapse of the Lagrangian bubbles feeds back onto the Eulerian carrier field
The bubble population attenuates the clean acoustic reverberations
Figure: Space-time diagram of axial centerline pressures at Mach 5. Left: Doped (); Center: Clean; Right: pressure difference.

## Slide 33: Doped Results: Pressure Perturbations
The perturbation signal is negligible during the initial shock transmission phase
The pressure perturbation fills the entire droplet
  Forms characteristic V-shaped or X-shaped diagonal bands
Figure: Space-time diagram of axial centerline pressure differences at Mach 3 at . Left: ; center:; right: .

## Slide 34: Doped Results: Pressure Perturbations
Figure: Heat maps of peak positive and negative pressure differences. Left: ; right: .
Peaks are highly dependent on Mach number (Mach ↑, ↑)
Peaks are highly dependent on bubble population ( ↑, ↑)

## Slide 35: Doped Results: Early Droplet Deformation
Figure: Numerical schlieren taken at doped cases with . Each frame shows comparison of respective clean half (left) and the doped half (right). Left: Mach 3; center: Mach 5; right: Mach 7.
There is nearly no observable difference* in surface deformation at any Mach or bubble density
  *Mach 7, ,
Noticeable damping of internal acoustics in doped cases with
Mach 3
Mach 5
Mach 7
Attenuation of acoustic reverberations

## Slide 36: Doped Results: Early Droplet Deformation

## Slide 37: Principal Findings
Main Conclusion: Pre-existing gas nuclei undergo strong internal activation, but this activation does not measurably alter early droplet-scale deformation over the tested parameter range, given the modeling assumptions.
Clean-droplet cases establish strong internal acoustic focusing
Gas nuclei are activated primarily by reflected tensile waves
Bubble growth is spatially selective
Dense populations produce acoustic attenuation and self-suppression of individual bubble growth
Despite strong local bubble dynamics and pressure perturbations, early interface deformation remains nearly unchanged

## Slide 38: Limitations and Future Work
Limitations:
Vapor production, condensation, and mass transfer were excluded
Bubble nuclei were fixed in space and did not advect with the liquid
Axisymmetric assumption limits 3D instability development
Conclusions are computational and require targeted experimental validation
Model extensions:
Add rate-limited phase-change models
Allow nuclei to advect with the liquid
Extend simulations beyond early-time axisymmetric regime
Extend nuclei modeling to solid/particulate inclusions and heterogeneous cavitation sites
Experimental direction:
Perform companion experiments with controlled nuclei populations

## Slide 39: Brendon A. Cavainolo¹, Rebecca Shannon², Sheryl M. Grace², and Michael P. Kinzel¹ ¹Department of Aerospace Engineering, Embry-Riddle Aeronautical University, Daytona Beach, FL, USA ²Department of Mechanical Engineering, Boston University, Boston, MA, USA This work was partially supported by the Air Force Office of Scientific Research under award number FA9550-22-1-0021. The author acknowledges DoD HPCMP and ERAU VEGA HPC use.
Acknowledgements